## Slide 1: STAT 524 Foliage classification using PCA Fall 2017 Behrokh Siamak

## Slide 2: Introduction
LiDAR* point cloud can be classified based on geometric characteristic.
Many applications are interested in tree detection using point cloud.
Objective
  To separate the points corresponding to foliage from other scanned points (point cloud).
  * LiDAR: Light Detection and Ranging
Notes: Agriculture – Urban designing – Environmental – Transportation

## Slide 3: Data collection platform
Stationary lasers scanners
Airborne platform
Mobile mapping platform
  provides an efficient/accurate way to sample the 3D road surrounding including notable roadside trees
Notes: Unmanned Aerial Vehicle – Manned Aerial Vehicle

## Slide 4: Study Area
Northwestern Ave, West Lafayette
  Length: 300 meters
  Northwestern Ave West Lafayette
  (Google map)

## Slide 5: Instrument specification
The dataset are acquired by HDL-32E
  ± 2 cm accuracy
  32 Channels
  80m-100m Range
  700,000 Points per Second
  360° Horizontal FOV
  +10° to -30° Vertical FOV
HDL-32E

## Slide 6: Data
  Data were collected on Oct 2016 by Digital Photogrammetry Research Group(DPRG)
  Return type: Single return
  Point number: 9,000,000 points
  Point density: 500 points/m^2
  Point cloud

## Slide 7: Methodology
This method works based on geometric characteristics of features
Point clouds were classified to ground/ non-ground
  Using LASTools
N-nearest neighbors using Kd-tree
  N= 70 (Lin, Benziger, and Habib, 2016)
Point Cloud
Ground/Non-ground
Kd-tree
N Nearest Neighbor
Notes: Linear – planner – volumetric

## Slide 8: Methodology _ Cont’d
Classify the points according to the geometrical shape of their neighborhood
  Principle Component Analysis (PCA)
    PCA approximates the spatial distribution of points in the neighborhood by an ellipsoid
Sample mean: =
) (
Singular value decomposition:
]
:

## Slide 9: Methodology _ Cont’d
  Center: sample mean
  Lengths
  Axis of ellipsoid:
  There are three extreme cases:
    1) >>>> (One main direction: linear neighborhood)
    2) ≈ (Two main directions: planar neighborhood)
    3) ≈ (Isotropy: volumetric neighborhood)
  (1)
  (2)
  (3)

## Slide 10: Methodology _ Cont’d
Three dimensionality descriptor:
    (Demantké et al., 2011)
  Linear descriptor : = (- )/
  (Responds on linear objects)
  Planar descriptor : = (- )/
  (Responds on planer objects)
  Volumetric descriptor : = /
  (Responds on volumetric objects)
  + + =1
PCA
Linear
Planar
Volumetric

## Slide 11: Methodology _ Cont’d
LPD/LPS
  Local point density is used to define a dynamic radius search for each point
=
=
=
  (Lin, Benziger, and Habib, 2016)
  Courtesy of Prof. Habib slides

## Slide 12: Methodology _ Cont’d
Run PCA again by a new neighborhood search radius based on LPD/LPS (r = 4 * LPS)
  Same criteria for classifying features
PCA (again)
Linear
Planar
Volumetric
Linear
Planar
Volumetric
LPD/LPS
LPD/LPS
LPD/LPS
r = 4 x LPS
Output from First PCA
Calculate

## Slide 13: Result
  Original Data
  Top View
  Side View

## Slide 14: Result _ Cont’d
  Fix 70 - NN
  Top View
  Side View

## Slide 15: Result _ Cont’d
  Dynamic radius (Considering LPS)
  Top View
  Side View

## Slide 16: Result _ Cont’d
  LAStools
  Top View
  Side View

## Slide 17: Conclusion
Detecting volumetric features using dimensionality PCA and considering LPD/LPS
Fix number in NN has noise
  Some planar or linear classified as volumetric features
LAStools seems is not proper to process ground mobile mapping data

## Slide 18: Limitation and Future work
Running algorithm is expensive in MATLAB
Having no ground truth
Developing
  Segmentation of the individual foliage
  To detect trunks

## Slide 19
Thank You!!

## Slide 20: Related Work
Demantké et al. (2011) used dimensionality PCA on a spherical neighborhood at various radius sizes to classify features to linear, planar, and rough (volumetric).
Lin, Benziger, and Habib (2016) applied threshold and dimensionality PCA to do planar based adaptive down-sampling using point local density (LPD) and local point spacing (LPS).